## Slide 1: Drew Beaudry
Arduino Piano
beaudryal18@uww.edu

## Slide 2: About the Project:
A project to teach children about music in a simple way.
An external interface to pick songs
5 buttons allow user to play notes
  Sound will be emitted on each press
Buttons will light up in the order to be played
  System will wait for user to play one note before lighting up the next

## Slide 3: Why?
I love music and believe in its importance.
Music Experience:
  My first instrument was a piano
    I moved onto Trumpet and then Guitar
  I’ve played guitar in two bands
  I’ve created electronic music in Ableton Live
  I’m a professional DJ with Midwest Sound

## Slide 4: Background
What is it?
  This is a 5 button light up keyboard that allows for Free-Play with the notes C4-G4
  There are also two programmed songs from the Legend of Zelda: Sarias’ Song and the Song of Storms
    These songs utilize more than 5 notes, as well as notes outside of the C4-G4 range
    We assign notes to colored buttons similar to Guitar Hero
How do I pick Songs?
  Connect to the device via Bluetooth
  Establish a connection with any Bluetooth Terminal
  Send the message ‘help’ to the device for a list of songs

## Slide 5: How?
Five 12v LED Buttons
  Each button has 4 terminals
    +/- for LED inside button
    2 terminals for a circuit to complete upon button press
  Cut and stripped 18 gauge wire and soldered to the terminals
  Attached 18 gauge wire to jumper cables via 18-22 gauge butt connectors

## Slide 6: How?
Powering the 12v buttons?
  12v 1 Amp Power supply
    Wall adapter to barrel jack – plug into Arduino
    Use “Vin” port on Arduino to access 12v power
  2N7000 N-Channel Metal-oxide-semiconductor field-effect transistor (NPN MOSFET)
    Supports up to 60v currents
    Gate threshold of 0.8 volts minimum
    Requires pull-down resistor to ground on gate
    When we want to give the button a 12v current, we send a signal to the gate to trigger the MOSFET as a switch
      Signal is sent via digitalWrite() from pins 2-7

## Slide 8: How?
How do we know what button is being pressed?
  In setup() we digitalWrite a HIGH signal to all buttons
  When a button is pressed it completes the circuit and a HIGH signal is sent back to the breadboard
  5 wires from Arduino pins A0-A4 are waiting for signals on the breadboard
  We digitalRead() on these pins constantly
  Pull down resistors exist between pins and input to keep readings accurate

## Slide 10: How?
Power tools! (and a Swiss Army Multi-tool)
  Had to drill 5 large holes for mounting the buttons
  Left space for an Android device on top
  Hand-Drilled a small hole for the power supply wire
  Used 3M Double sided tape for mounting devices

## Slide 11: How?
Bluetooth?
  HC-05 Bluetooth module
  Connects to Arduino via pins 0 and 1
    TX and RX pins
    Problem: Arduino sends data to Bluetooth module from TX pin 1 at 5v, and Bluetooth module is rated for 3.5v signals
      Voltage divider using 2k & 5K1 resistors
        Turns 5v into 3.59v
  Phone and Arduino communicate each with each other via Strings in Serial Monitor
    Serial.available() tells us when we have a message waiting
    Serial.readString() reads the message
    String.indexOf() can tell us what the message contains

## Slide 13: How?
Sound?
  Using the provided buzzer in the kit
  Problem: Its not loud enough!
    Solution: Increased power to 5 volts
      Used NPN Transistor in kit as a switch to provide voltage from 5v pin on Arduino
  Used a library which provided a frequency for every note from B0-D#8
  Used a modified digitalWrite from pin 9 to buzzer
    Created a sort of PWM signal with shown methods
    Regular PWM was not sounding great

## Slide 14: Code: (Music)

## Slide 15: Code: (Music)

## Slide 16: Code: (Bluetooth)

## Slide 21: Compared to a Similar Product
https://www.instructables.com/id/Capacitive-Touch-Arduino-Keyboard-Piano/
My inspiration for this project
  An instructable article which detailed a Capacitive-Touch Arduino Keyboard Piano
  Uses a 5v signal sent to all aluminum foil keys
    Senses when a finger presses the keys and plays a note on the buzzer
  I borrowed the idea of a “common send” voltage to all buttons
    Initially I wanted to AnalogWrite different frequencies to each button and read all buttons on a single pin
    This approach proved much more simple and I still have pins to spare
  I also borrowed the library of different note frequencies

## Slide 22: Future Work:
A full Android App
  Easy, clickable buttons quick send Bluetooth commands
  This will make the project more child friendly
  I researched a solution provided by MIT called App Inventor
    Allows anyone to build apps quickly
    Used in Bluetooth to Android examples I’ve seen
    Create an app via the web and produce a code to pair the app to your phone
  I will soon be developing Kotlin in IntelliJ
    The Android SDK was recently switched from Eclipse IDE to IntelliJ and Kotlin development for Android is possible
    In the future I can build a full-fledged application and use it to store and communicate data for several songs

## Slide 23: Demonstration Video:
https://www.youtube.com/watch?v=F7LMoaXS20Q&feature=youtu.be